## Slide 1: Floating Point
CSCI3240: Lecture 4 and 5
Dr. Arpan Man Sainju
Middle Tennessee State University

## Slide 2: Representing Real Numbers in Binary
Carnegie Mellon
What is 2?
Let's first understand what fixed point binary is.
Next, we will learn what floating point binary is.

## Slide 3: Fixed Point Binary Fractions
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
Represents fractional part
of the real number
We can use an imaginary binary point to separate whole number from fractional part.
The position of the binary point is fixed and can’t be moved.
In this example, 9-bits are used to represent whole number portion and 7 bits are used to represent fractional part.
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
Whole number portion of real number

## Slide 4: Converting Fixed Point Binary to Denary
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
Converting the whole portion:
Converting the fractional portion:

## Slide 5: Another Example
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0
Converting the whole portion:
Converting the fractional portion:

## Slide 6: Practice Questions
The following binary numbers are stored using two’s complement in a 12-bit register with 4 bits after the binary point. Convert them into decimal fraction.
010001111010
111111111111
100001110010

## Slide 7: Practice Questions
Using two’s complement, convert the following decimal numbers into fixed point binary to be stored in a 12 bit register with 4-bit after the binary point.
27.5
-55.75
-1.75
0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0

## Slide 8: Observation
Given a 4-bit register, with 1-bit before and 3-bit after the binary point, using two’s complement, calculate:
The largest positive number that can be represented is
The smallest positive number that can be represented (not including 0)
0 | 1 | 1 | 1
0 | 1 | 1 | 1
0 | 0 | 0 | 1
0 | 0 | 0 | 1

## Slide 9: Observation
Given a 4-bit register, with 1-bit before and 3-bit after the binary point, using two’s complement, calculate:
The smallest magnitude negative number that can be represented (closet to 0)
The largest magnitude negative number that can be represented
1 | 1 | 1 | 1
1 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 0

## Slide 10: Summary
Fixed point binary is used in digital signal processing.
It is employed when performance is more important than accuracy.
  Gaming
Simple and cheaper processor hardware
Faster processing
Tradeoff between range and precision
Some numbers can never be represented accurately. Such as 1/10.

## Slide 11: Floating Point Binary
Standard Scientific Notation
  Speed of light
  Avogadro’s number
  Charge of electron

## Slide 12: Floating Point
Number written in scientific notation have three components:
  X
sign
Mantissa
Exponent
Sign
(by default, positive)
Mantissa
Exponent
X
The number of digits that you are allowed to use in Mantissa governs the precision of values.
The number of digits available for exponent governs the range. For 2 digits you can only float the point up to 99 places.

## Slide 13: IEEE 754 Standard for Floating-Point Representation
Number written in scientific notation have three components:
  X
Three fields:
  Single precision: 1-bit (sign), 8-bit (exponent), 23-bit (Mantissa) : 32-bits total
  Double precision: 1-bit (sign), 11-bit (exponent), 52-bit (Mantissa) : 64-bits total
Sign
Exponent
Mantissa
1 Bit
8 Bit
23 Bit
Sign
Exponent
Mantissa
1 Bit
11 Bit
52 Bit
sign
Mantissa
Exponent
Mantissa: fraction part of a floating-point number

## Slide 14: IEEE 754 Standard for Single Precision 32-bit floating point binary
Sign bit
1-bit
8-bit
Exponent
23-bit
Mantissa
Convert the real number 27.236875 into IEEE 7544 standard 32-bit floating point binary
Step 1: Determine the sign bit (0 if positive, 1 if negative)
Sign bit = 0
Step 2: Convert to pure binary
A. Converting whole number part. B. Converting the fractional part
Stop when product is 1
0

## Slide 15: IEEE 754 Standard for Single Precision 32-bit floating point binary
0 |  |  |  |  |  |  |  | 
Sign bit
1-bit
8-bit
Exponent
23-bit
Mantissa
Convert the real number 27.2185 into IEEE 754 standard 32-bit floating point binary
Step 3: Normalize to determine the Mantissa and the unbiased exponent
- place the binary point after leftmost 1
Step 4: Determine the biased exponent (K = number of bits in exponent)
- add bias () 127 then convert to an 8-bit unsigned binary integer
Step 5: Remove the leading 1 from the Mantissa
- remove the leftmost 1
Note:
the left most bit of Mantissa is always going to be 1. (see step 3)
No need to store it.
We get extra 1-bit precision
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 16: Why do we need to add bias to the exponent?

## Slide 17
Assume 4-bit
exponent
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 1
Only +ve
exponents
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Two’s
complement
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
7
8
9
10
Changing range
-9
-8
-7
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
IEEE 754 Standard
-7
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
7
8
Slightly favors positive numbers
Here, bias is 7 because we have 7 -ve numbers.
We have to add bias to convert the number into unsinged binary for IEEE 754 standard.
-7 +7 = 0
-6 +7 = 1
-5+7 = 2
6 + 7 = 13

## Slide 18: Exponent bias
IEEE 754 Format | Sign | Exponent | Mantissa | Exponent Bias
32 bit single precision | 1 bit | 8 bit | 23 bits (+1 not stored) | 
64 bit double precision | 1 bit | 11 bit | 52 bits (+1 not stored) | 
IEEE 754 Format | Sign | Exponent | Mantissa | Exponent Bias
32 bit single precision | 1 bit | 8 bit | 23 bits (+1 not stored) | 
64 bit double precision | 1 bit | 11 bit | 52 bits (+1 not stored) | 

## Slide 19: Why not use Two’s complement instead of IEEE 754 Standard for exponent?
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 1
Two’s complement
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
IEEE 754 Standard
-7
-6
-5
-4
-3
-2
-1
0
1
2
3
4
5
6
7
8
With IEEE 754 standard the computer can easily identify if one number is bigger then another by just looking at the bit pattern.
It is not possible with 2’s complement.
See 7 and -8.

## Slide 20: Practice Questions
Convert 0.6875 into IEEE 754 single precision floating point binary
  Step 1: Determine the sign
  Step 2: Convert to pure binary
  Step 3: Normalize for Mantissa and unbiased exponent
  Step 4: Determine biased exponent
  Step 5: Remove leading 1 from Mantissa

## Slide 21: Practice Question
Convert -123.84375 into IEEE 754 single precision floating point binary
  Step 1: Determine the sign
  Step 2: Convert to pure binary
  Step 3: Normalize for Mantissa and unbiased exponent
  Step4: Determine biased exponent
  Step5: Remove leading 1 from Mantissa

## Slide 22: Converting back to decimal
Determine the sign in decimal
Determine the exponent in decimal
Remove the exponent bias
  Subtract (), where k is number of bits in exponent field.
Convert the Mantissa to decimal
Add 1 to the Mantissa and include the sign
Compute the final result.

## Slide 23: Practice Question
Convert 01000001001101010000000000000000 into decimal

## Slide 24: Practice Question
Convert 10000001001000110010000000000000 into decimal

## Slide 25: Reserved Exponent Values
Exponent Values | Mantissa | Represents
11111111 | All zeros | 
11111111 | Not all zeros | 
00000000 | All zeros | Zero
Exponent Values | Mantissa | Represents
11111111 | All zeros | 
11111111 | Not all zeros | 
00000000 | All zeros | Zero

## Slide 26: Floating Point Operations: Basic Idea
Carnegie Mellon
x +f y = Round(x + y)
x f y = Round(x  y)
Basic idea
  First compute exact result
  Make it fit into desired precision
    Possibly overflow if exponent too large
    Possibly round to fit into Mantissa fraction

## Slide 27: Rounding
Carnegie Mellon
Rounding Modes (illustrate with $ rounding)
$1.40 $1.60 $1.50 $2.50 –$1.50
  Towards zero $1 $1 $1 $2 –$1
  Round down (−) $1 $1 $1 $2 –$2
  Round up (+) $2 $2 $2 $3 –$1
  Nearest Even (default) $1 $2 $2 $2 –$2

## Slide 28: Rounding Binary Numbers
Carnegie Mellon
Binary Fractional Numbers
  “Even” when least significant bit is 0
  “Half way” when bits to right of rounding position = 100…2
Examples
  Round to nearest 1/4 (2 bits right of binary point)
  Value Binary Rounded Action Rounded Value
  2 3/32 10.000112 10.002 (<1/2—down) 2
  2 3/16 10.001102 10.012 (>1/2—up) 2 1/4
  2 7/8 10.111002 11.002 ( 1/2—up) 3
  2 5/8 10.101002 10.102 ( 1/2—down) 2 1/2

## Slide 29: FP Multiplication
Carnegie Mellon
(–1)s1 M1 2E1 x (–1)s2 M2 2E2
Exact Result: (–1)s M 2E
  Sign s: s1 ^ s2
  Mantissa M: M1 x M2
  Exponent E: E1 + E2
Fixing
  Normalize (move decimal point after first 1)
  If E out of range, overflow
  Round M to fit Mantissa fraction precision
Implementation
  Biggest chore is multiplying Mantissas

## Slide 30: Floating Point Addition
Carnegie Mellon
(–1)s1 M1 2E1 + (-1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (–1)s M 2E
  Sign s, Mantissa M:
    Result of signed align & add
  Exponent E: E1
Fixing
  Normalize (move decimal point after first 1)
  Overflow if E out of range
  Round M to fit Mantissa fraction precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M
Get binary points lined up

## Slide 31: Mathematical Properties of FP Add
Carnegie Mellon
Compare to those of Abelian Group
  Closed under addition?
    But may generate infinity or NaN
  Commutative?
  Associative?
    Overflow and inexactness of rounding
    (3.14+1e10)-1e10 = 0, 3.14+(1e10-1e10) = 3.14
  0 is additive identity?
  Every element has additive inverse?
    Yes, except for infinities & NaNs
Monotonicity
  a ≥ b ⇒ a+c ≥ b+c?
    Except for infinities & NaNs
Yes
Yes
Yes
No
Almost
Almost

## Slide 32: Mathematical Properties of FP Mult
Carnegie Mellon
Compare to Commutative Ring
  Closed under multiplication?
    But may generate infinity or NaN
  Multiplication Commutative?
  Multiplication is Associative?
    Possibility of overflow, inexactness of rounding
    Ex: (1e20*1e20)*1e-20= inf, 1e20*(1e20*1e-20)= 1e20
  1 is multiplicative identity?
  Multiplication distributes over addition?
    Possibility of overflow, inexactness of rounding
    1e20*(1e20-1e20)= 0.0, 1e20*1e20 – 1e20*1e20 = NaN
Monotonicity
  a ≥ b & c ≥ 0 ⇒ a * c ≥ b *c?
    Except for infinities & NaNs
Yes
Yes
No
Yes
No
Almost

## Slide 33: Floating Point in C
Carnegie Mellon
C Guarantees Two Levels
  float single precision
  double double precision
Conversions/Casting
  Casting between int, float, and double changes bit representation
  double/float → int
    Truncates fractional part
    Like rounding toward zero
    Not defined when out of range or NaN: Generally sets to TMin
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size
  int → float
    Will round according to rounding mode

## Slide 34: Floating Point Puzzles
Carnegie Mellon
For each of the following C expressions, either:
  Argue that it is true for all argument values
  Explain why not true
x == (int)(float) x
x == (int)(double) x
f == (float)(double) f
d == (double)(float) d
f == -(-f);
2/3 == 2/3.0
d < 0.0 ⇒ ((d*2) < 0.0)
d > f ⇒ -f > -d
d * d >= 0.0
(d+f)-d == f
int x = …;
float f = …;
double d = …;
Assume neither
d nor f is NaN